## Slide 1: A hands-on introduction to Multiple Point Statistics
Gregoire Mariethoz, Mathieu Gravey, Fabio Oriani
University of Lausanne, GAIA Lab

## Slide 2: Context: dealing with data in geosciences
Main challenges:
Natural phenomena vary in space and in time
Data are typically incomplete
No matter how sophisticated the data acquisition methods
Examples:
Point data need to be interpolated on a grid
The available data are too coarse (need downscaling)
Data present spatial or temporal gaps (e.g. gaps in time series, holes in images)
Approach often used to deal with the lack of data: geostatistics.

## Slide 3: Many problems in geosciences: Strong spatial variability+lots of data

## Slide 4: Some typical problems
Gap-filling
Data fusion/downscaling
Landsat 7 SLC-off gaps

## Slide 5: Interpolation with lots of information
Lots of information: local, textural, etc.
Parametric models such as kriging are parsimonious (2-3 perameters).
This parsimony leads to information loss.
Main issue: the interpolated samples are only as rich as the model (thus poorer than the original data).

## Slide 6: Training images in action
Probability of encountering a channel (white)
Realization 1
Realization 2
Generate spatially continuous textures, with correct statistics
Notes: Here is an example with a training image corresponding to a remote sensing image of the Ganges delta.
It is used to build models that present the same spatial patterns and that respect given data.
Several models possible, thus allowing to quantify uncertainty.

## Slide 7: Multiple-point geostatistics
Based on 3 main concepts:
When the features to model are too complex for parametric models, use non-parametric models.
Capturing complex features requires lots of data. When these data are not available, we can use analogues, which can be expressed as training images.
To capture complexity, it is not sufficient to look at the relationships between pairs of locations, but one should compare entire patterns.
First proposed in 1993:
Guardiano, F. and M. Srivastava (1993). Multivariate geostatistics: Beyond bivariate moments. Geostatistics-Troia. A. Soares. Dordrecht, Kluwier Academic. 1: 133-144.
The concept really became popular only 10-15 years later.

## Slide 8: Pattern matching
Fundamental principle of multiple-point geostat: pattern matching.
Given a neighborhood pattern Nx, we look for a similar pattern Ny in the training image.
This is done using a distance or mismatch:
Repeat until a complete texturized image is generated.

## Slide 9: The DS algorithm (not use today)
Simulation
neighborhood
As soon as one good configuration is found,
the value at the central pixel is assigned to the simulated node.
Training image
Doesn’t match
Matches !
Doesn’t match
Copy the value

## Slide 10: Sequential simulation
Video R. Nussbaumer

## Slide 11: Definition of the data event
Data event constituted of the n closest nodes. Adapts automatically with the density of informed grid nodes.
Able to automatically represent multiple scales.

## Slide 12: Can be used with continuous variable
Mariethoz, G., et al. (2010). "The direct sampling method to perform multiple-point geostatistical simulations." WRR 46(11).

## Slide 13: Extension to multiple variables

## Slide 14: The QS algorithm Used today - equivalent to DS but faster
Simulation
neighborhood
Select randomly one of the k best candidates
Training image
Copy the value
Matches !

## Slide 15: The QS algorithm
For each simulated pixel, a full mismatch map is generated.
The k best matches are selected
One of these k matches is sampled
Gravey, M. and G. Mariethoz (2020). "QuickSampling v1.0: a robust and simplified pixel-based multiple-point simulation approach." Geosci. Model Dev. 13(6): 2611-2630.

## Slide 16: Parameters
QS has two parameters to control the importance of neighbors:
the number of neighbors considered, always the closest.
The , that weights the importance of each position in the neighborhood.
QS has a single parameter that controls the variability:
k the number of best candidates
:
Neighbors outside the circle have a weight of 0
x0.5: kernel
x0.5: kernel
x2: kernel

## Slide 17: Sensitivity to k and n

## Slide 18: Sensitivity to kernel

## Slide 19: Some case studies

## Slide 20: Satellite image gap-filling
Landsat-7: 15 years of continuous imaging with gaps.
Training image is the non-gap areas.
Quantification of the reconstruction uncertainty through multiple realizations.
Blue
Green
Red
Near IR
Short IR

## Slide 21: Application to Landsat 7 SLC-off images
Yin, G., et al. (2017). "Gap-filling of landsat 7 imagery using the direct sampling method." Remote Sensing 9(1).

## Slide 22: Downscaling satellite imagery
Lower portion of the image only known with low-quality sensor
Lower portion of the image reconstructed using MPS
Oriani, F., M. F. McCabe and G. Mariethoz (2021). "Downscaling Multispectral Satellite Images Without Colocated High-Resolution Data: A Stochastic Approach Based on Training Images." IEEE Trans. on Geo. Rem. Sen. 59(4): 3209-3225.

## Slide 23: Time series simulation
Time [days]
Rainfall amount [mm]
Time [days]
Rainfall amount [mm]

## Slide 24
600
800
1000 days
Multivariate rainfall simulation
Oriani, F., R. Mehrotra, G. Mariethoz, J. Straubhaar, A. Sharma and P. Renard (2018). "Simulating rainfall time-series: how to account for statistical variability at multiple scales?" Stochastic Environmental Research and Risk Assessment 32(2): 321-340.

## Slide 25: Statistics of simulations
Annual seasonality
Mean daily rainfall [mm]
Daily rainfall standard deviation [mm]
Darwin
Sydney
Wet day occurrence probability
Alice Springs

## Slide 26: Properties of MPS simulations
The texture is borrowed from an analogue.
The Generated patterns are non-smooth and texturally complex (i.e. patterns with sharp transitions, well-defined shapes and objects).
Reproduction of non-smooth features is quantified with texture metrics (spatial covariance, connectivity, coherence of classes).
Different stochastic realizations allow exploring uncertainty.

## Slide 27: Conclusions
MPS can be useful when one needs to generate complex patterns, and at the same time large amounts of analogue data are available elsewhere (=prior information).
Challenges remain regarding the source of training images, the parameterization of simulation algorithms, and in some cases computing cost.
Other applications exist, e.g. downscaling, weather generation, data fusion, 3D subsurface models.
Open-source code here: https://github.com/GAIA-UNIL/G2S

## Slide 28
https://gaia-unil.github.io/G2S/
https://gmd.copernicus.org/articles/13/2611/2020/

## Slide 29
Thank you
Questions?